## Slide 1
1/4" Male mono ["Interpretation Console Jack"]
1/8" Male stereo ["Williams Sound console jack"]
1/4" Male stereo (90 degree angle is nicer)
["Compressor Jack"]
Just take the tip from the stereo Williams Sound jack
Connect to the ring of the compressor jack
1/4" Female mono (optional)
1/8" Female stereo (tip and ring on same cable) ["Headphone Jack"]
A
B
Schematic for Audio Compressor Cable
Try to keep distances short between Point A and all connectors, to avoid having an octopus-like blob of wires
Between Points A and B, just one cable, about 4 feet long.
Connect to the tip of the compressor jack

## Slide 2
1/4" M mono
1/8" M stereo
1/4" M stereo
(coudé si possible)
Prendre seulement le "tip" du stereo
Connecter au "ring" du stereo
1/4" F mono
1/8" F stereo
("tip" et "ring" sur même fil)
A
B
Schéma de filage pour cable de compresseur audio
"Bouquet de connecteurs" le moins "tentaculaire" possible (distances courtes entre connecteurs et point A)
Entre points A et B, un seul cable, d'une longueur d'environ 4 pieds.
Stefan Jetchick, 418-922-7015
Connecter au "tip" du stereo